## Slide 1
FIELD TRAINING
How to read a coax hardline print
A night-by-night tutorial: what you were given, where it is, and what to do there.
WHAT YOU GOT
The work that came in tonight and what you need to pull from it.
WHERE IT IS
How to find that work on the map — street, then house number.
WHAT TO DO
How to read the notes at that spot and stay in your scope.
FBR Internal Use Only · Every night and every market is different · Learn the method, not one job

## Slide 2
What we are going over
AGENDA
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
2
01
Understand the work you receive each night
What shows up on your assignment, what you need to take from it, and what you don’t need yet.
02
Learn the legend and the labels first
Letters, symbols, and numbers on the print — poles, taps, actives, and tags — before you hunt streets.
03
Open the right map and find the job site
Match tonight’s work to the correct print, then street, then house number, then the device.
04
Read the notes at that location
How to use notes and callouts to see what that pole needs — and when to leave it alone.
05
Do only the work that was assigned
Jobs change every night and every market. Tonight’s list and the notes decide, not last night’s habit.
06
Practice the steps on sample maps
We’ll walk example prints so you can run the process. The samples are practice, not “the” job.

## Slide 3
Start here: the work-letter legend
LEGEND
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
3
Before you look for a street, know what the letters on the print mean. A letter on a device is the work at that spot.
A
Swap the active
Replace the amp or node that is already there.
E
New tap
Install a new tap. The number in the circle is the tap value.
G
New splitter
Install a new splitter on that branch.
H
Add an active
Put in an amp that was not there before.
J
EQ comes out
Remove the equalizer. The print may show a jumper left in.
More than one letter at one spot
If the box says A, E — swap the active and put a new tap there. If it says J and add splice — do both. Read the whole string. Then check your assignment: if that device is not yours, you still don’t work it.

## Slide 4
Start here: symbols on the print
LEGEND
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
4
These are the hardware marks you’ll see on the line. Same idea every market — the drawing style can vary a little, the meaning does not.
×
Pole
Circle with an X. Strand plant hangs here. This is a location, not a tap.
17
Tap
Circle with a number. That number is the tap value (dB), not the house and not the pole ID.
Active / amp
Triangle on the line. Powered device. Black corners = input / bridger style — not a splitter. Next slide shows the variants.
Node
Heavier box, often with triangles. Fiber-to-coax point for that area. Not every night is a node swap.
Splitter
Junction on the line where one hardline becomes two. Work letter G if it’s new.
S 14
Splice
Box or mark with S (sometimes S 14). Hardline is joined here. Notes may say add / resplice.
Power
Supply or inserter. You may see 90V, amps, or a bolt. Only your job if it was assigned.
×
Ped / cabinet
Square or box on the ground path. Buried plant, not a pole. Same idea: find the address first.

## Slide 5
Triangles and circles — what they actually are
LEGEND
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
5
Triangle + black corners
AMPLIFIER (active). The filled corners mark the output legs. Bridger / mini-bridger style. Not a splitter.
Open / regular triangle
AMPLIFIER too — usually a line extender (one output). Same family as the black-corner triangle.
Filled / solid circle
TERMINATOR. Caps a dead-end or unused port. Notes may say ADD TERM.
Empty circle
Often just a pole or a simple junction. Don’t treat it as a tap unless it has a value in it.
+
Circle with + or ×
POLE. Strand plant hangs here. The address is still the gray number in the lot.
Half-filled circle + x
POWER at that device — power passing or a power inserter. Only your job if it was assigned.
2
Circle with a small number
If it’s 4, 8, 11, 14, 17, 20, 23, 26 — that’s TAP VALUE. A 1–4 next to a house is how many drops, not the tap.
Splitter (for comparison)
A splitter is a junction that splits the hardline. Work letter G. It is passive with no gain different from a dual output
x

## Slide 6
Start here: lines and marks on the print
LEGEND
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
6
The linework tells you how plant is built. The marks next to it tell you where you are and what work is called.
Hardline
Thick solid line along the street. This is the coax you splice — not the drop to the house.
Drop / service
Thinner line or tick toward a lot. That’s the house feed, not the mainline.
142'
Footage
Number with a foot mark (142'). Distance to the next device. Not the address.
176
House number
Gray number sitting in the lot. Street + this number is where you park.
A6
Device ID
Small tag like A6 or E12. Match it to tonight’s assignment. This is the name, not the work.
E
Work letter
Letter box on a device (A, E, G…). That’s the work at that spot — if it’s on your list.
NOTE
Note / callout
Text with an arrow. Read it before you open anything. It can say stop, splice, or leave it.
Node boundary
Heavy colored line. Work stops here unless that node is on tonight’s assignment.

## Slide 7
Start here: the labels on the map
LEGEND
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
7
Four kinds of numbers sit next to each other. Learn this before you hunt a job site. Only one of them is the address.
176
GRAY NUMBER IN THE LOT
HOUSE / ADDRESS
This is where you park. Street + this number is the job site.
176'
NUMBER WITH A FOOT MARK
FOOTAGE
How far along the line to the next device. Not the house.
17
NUMBER INSIDE A CIRCLE
TAP VALUE
The tap at that spot, if that tap is yours. Not the address.
A6
SMALL TAG BY A DEVICE
DEVICE ID
The name of that amp or tap. Match it to tonight’s assignment.

## Slide 8
What a print looks like — add your arrows here
THE MAP
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
8
Use this slide for overlays
Point arrows at: • Pole (circle + X) • Street name • House / lot number • Tap (circle + value) • Amp / node • Splice / splitter • Work letter + note This is a sample print. Tomorrow’s map will be a different node and a different town.

## Slide 9
A closer look — street, lot, device, note
THE MAP
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
9
Label this close-up
Good overlay order: 1. Street 2. House number 3. The device on that lot 4. The work letter 5. The note pointing at it If you can mark those five things on any print, you can find the job.

## Slide 10
Understand the work you receive each night
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
10
You do not need the whole print yet. You need tonight’s list. That list changes. The way you read it does not.
What to take from the assignment
Node or area name, the device IDs that are yours, and the count (how many actives, taps, splices). Write them down before you open the map.
What you can ignore for now
Other people’s names, other crews’ counts, and any extra columns that don’t help you find a street. Come back to those only if a lead adds scope.
What will be different tomorrow
The node, the town, the hardware, even the filename. Don’t memorize one sample job. Memorize: list → right map → address → notes.
How you know you’re ready to open the map
You can say out loud: “I have these device IDs on this node.” If you can’t, you’re not ready to hunt streets.

## Slide 11
Open the right map for that work
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
11
Check these before you hunt
1. The node / area on the print matches tonight’s assignment. 2. You’re in the right town / hub — street names should look familiar for where you were sent. 3. Find the box with your company or name. That box is your count for this print. 4. If the node doesn’t match the sheet, you have the wrong file. Close it. Filenames vary by market. Don’t rely on the name alone — confirm the node on the print.

## Slide 12
Find the job site: street, then house number, then the device
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
12
The order
1. Street name — that’s how you stage the truck. 2. Gray number in the lot — that’s the address. Park here. 3. Device on that lot — amp, tap, splitter. 4. Device tag — does it match an ID on tonight’s list? If the street is wrong, stop. Don’t “fix it” by working the next block over. Add arrows on this map for street and house numbers.

## Slide 13
Same method on a different sample print
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
13
Practice overlay
Pick one assigned device on this sample and mark: • The street • The house number • The device • Whether it’s on tonight’s list If you can’t find the house number, you’re not ready to climb.

## Slide 14
Read the notes at that location before you work
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
14
What notes are for
A note on the print beats a guess. Common ones you’ll see: • Work at this pole (splice, term, swap) • This area is another node — leave it • Already complete — don’t reopen it • Power / plant-wide instruction Read the print-wide note first, then the arrows at your devices. If a note and your assignment disagree, stop and ask. Don’t invent scope.

## Slide 15
Do only the work that was assigned
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
15
Tonight’s job
1. You’re on the right street and house number. 2. The device tag matches an ID on your list. 3. You read the notes pointing at that device. 4. You do the work listed for you at that spot. 5. On AOI high-split actives, let it auto-balance unless that job or a lead says otherwise. 6. Close it out. Don’t add extra plant because you were already there.
Not automatically yours
Node swaps, power upgrades, a street full of taps, splices, EQ removals — only if they’re on your list or a lead adds them. Last night may have been a mini-bridger. Tonight may be taps, a splice, or a different market’s hardware. The method stays the same. The work does not.

## Slide 16
The order — every night, every market
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
16
1
Read tonight’s assignment
Write the node and the device IDs that are yours.
2
Open the matching print
Confirm the node on the print matches the sheet.
3
Use the legend
Know the letters and which number is the address.
4
Find the job site
Street, then house number, then the device on that lot.
5
Read the notes
Print-wide note, then the callouts at your devices.
6
Do assigned work
Only what’s on your list. Auto-balance when that’s the job.

## Slide 17
Practice: find assigned work on this sample
PRACTICE
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
17
Review the Network Evolution Excel Sheet
This sheet will contain a list of all the assigned techs for that nights work and what work they were issued. 1. Format : NODE-AMPID (SOME MAY CONTAIN AN UNDERSCORE)
2. You will take this ID and go to the map (AFTER PRINT) to find the Tag #
3. Use the Tag # to find the location on the map and find the closest address.
4. Enter the address in your work phone maps and head there!

## Slide 18
Practice: same steps, different sample
PRACTICE
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
18
What to mark
This sample has a different layout, different streets, and work that belongs to more than one crew. Mark: • A node boundary / “leave it” note • One assigned device and its house number • One note that is not your work If you can tell “mine” from “not mine” on a busy print, you’re reading it right.

## Slide 19
Where people get it wrong
TUTORIAL
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
19
Starting in the middle of the map
Open the assignment first. If you don’t know tonight’s IDs, the streets won’t help you.
Wrong print
The file on the tablet isn’t automatically tonight’s node. Confirm the node on the print matches the sheet.
Treating a tap value as an address
The circle is not the house. The gray number in the lot is where you park.
Working another crew’s devices
A print can be covered in work letters. Yours are the ones on your list.
Ignoring a leave-it note
Another node, already complete, or past a boundary — don’t reopen it.
Assuming last night’s setup
Not every job is the same amp or the same market. Read this job. Auto-balance when that’s what you were given.

## Slide 20
Quick reference
KEEP THIS SLIDE
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
20
1
Assignment
2
Right map
3
Legend
4
Address
5
Notes
6
Work
Circle with an X
Pole — strand location
Circle with a number
Tap value — not the house
Triangle / heavy box
Active or node
S 14 / junction
Splice or splitter
Gray number in the lot
Address — park here
Letter box + note
Work at that spot, if it’s yours
DO
Take tonight’s IDs off the assignment first. Confirm the node on the print. Park on the house number. Read notes at that pole. Do only what’s on your list.
DON’T
Start in the middle of the streets. Treat a circle as an address. Work another crew’s letters. Assume last night’s hardware or setup. Guess when the sheet and print don’t match.

## Slide 21
Check that you can do this
PRACTICE
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
21
1. You just got tonight’s assignment. What do you write down before you open a map?
2. You’re on a lot labeled 23. Next to it is a circle with 23. Where do you park, and what is the circle?
3. Your list is two actives. The print is covered in work letters. Which devices do you work?
4. A note says this area belongs to another node, or is already complete. What do you do?
5. Last night was a mini-bridger. Tonight’s list is taps in a different market. What stays the same?
6. The print on the tablet doesn’t match the node on your sheet. What’s the next step?
Answers on the next slide. If two or more are shaky, run a sample print with a supervisor before you take a truck.

## Slide 22
Check — answers
PRACTICE
INTERNAL TRAINING
FBR · How to read a coax hardline print · Company Confidential
22
1
The node / area and the device IDs that are yours — plus the count. That’s the target list.
2
Park at house 23. The circle is the tap value, not the address.
3
Only the devices on your list. The rest of the letters belong to other crews or other nights.
4
Leave it. Don’t reopen finished plant and don’t work another node.
5
The method: assignment → right map → legend → address → notes → assigned work. The hardware can change.
6
Wrong file. Close it and open the print that matches tonight’s node. Don’t start from the streets.

## Slide 23
YOU’RE READY WHEN YOU CAN DO THIS ON ANY PRINT
Know tonight’s work. Find the address. Do that job.
Write the IDs, open the matching map, use the legend, park on the house number, read the notes, and stay in your scope. Tomorrow will be a different night.
Tonight’s IDs are written down
The print matches that node
Parked on the house number
Notes read — only assigned work done
FBR · Internal training · If the sheet and the print don’t agree, stop and call a supervisor